## Slide 1: Chapter 9: Main Memory

## Slide 2: Chapter 9: Memory Management
Background
Contiguous Memory Allocation
Paging
Structure of the Page Table
Swapping
Example: The Intel 32 and 64-bit Architectures
Example: ARMv8 Architecture

## Slide 3: Objectives
To provide a detailed description of various ways of organizing memory hardware
To discuss various memory-management techniques,
To provide a detailed description of the Intel Pentium, which supports both pure segmentation and segmentation with paging

## Slide 4: Background
Program must be brought (from disk) into memory and placed within a process for it to be run
Main memory and registers are only storage CPU can access directly
Memory unit only sees a stream of:
  addresses + read requests, or
  address + data and write requests
Register access is done in one CPU clock (or less)
Main memory can take many cycles, causing a stall
Cache sits between main memory and CPU registers
Protection of memory required to ensure correct operation

## Slide 5: Protection
Need to censure that a process can access only those addresses in its address space.
We can provide this protection by using a pair of base and limit registers define the logical address space of a process

## Slide 6: Hardware Address Protection
CPU must check every memory access generated in user mode to be sure it is between base and limit for that user
the instructions to loading the base and limit registers are privileged

## Slide 7: Address Binding
Programs on disk, ready to be brought into memory to execute form an input queue
  Without support, must be loaded into address 0000
Inconvenient to have first user process physical address always at 0000
  How can it not be?
Addresses represented in different ways at different stages of a program’s life
  Source code addresses usually symbolic
  Compiled code addresses bind to relocatable addresses
    i.e., “14 bytes from beginning of this module”
  Linker or loader will bind relocatable addresses to absolute addresses
    i.e., 74014
  Each binding maps one address space to another

## Slide 8: Binding of Instructions and Data to Memory
Address binding of instructions and data to memory addresses can happen at three different stages
  Compile time: If memory location known a priori, absolute code can be generated; must recompile code if starting location changes
  Load time: Must generate relocatable code if memory location is not known at compile time
  Execution time: Binding delayed until run time if the process can be moved during its execution from one memory segment to another
    Need hardware support for address maps (e.g., base and limit registers)

## Slide 9: Multistep Processing of a User Program

## Slide 10: Logical vs. Physical Address Space
The concept of a logical address space that is bound to a separate physical address space is central to proper memory management
  Logical address – generated by the CPU; also referred to as virtual address
  Physical address – address seen by the memory unit
Logical and physical addresses are the same in compile-time and load-time address-binding schemes; logical (virtual) and physical addresses differ in execution-time address-binding scheme
Logical address space is the set of all logical addresses generated by a program
Physical address space is the set of all physical addresses generated by a program

## Slide 11: Memory-Management Unit (MMU)
Hardware device that at run time maps virtual to physical address
Many methods possible, covered in the rest of this chapter

## Slide 12: Memory-Management Unit (Cont.)
Consider simple scheme. which is a generalization of the base-register scheme.
  The base register now called relocation register
The value in the relocation register is added to every address generated by a user process at the time it is sent to memory
The user program deals with logical addresses; it never sees the real physical addresses
  Execution-time binding occurs when reference is made to location in memory
  Logical address bound to physical addresses

## Slide 13: Memory-Management Unit (Cont.)
Consider simple scheme. which is a generalization of the base-register scheme.
  The base register now called relocation register
The value in the relocation register is added to every address generated by a user process at the time it is sent to memory

## Slide 14: Dynamic Loading
The entire program does need to be in memory to execute
Routine is not loaded until it is called
Better memory-space utilization; unused routine is never loaded
All routines kept on disk in relocatable load format
Useful when large amounts of code are needed to handle infrequently occurring cases
No special support from the operating system is required
  Implemented through program design
  OS can help by providing libraries to implement dynamic loading

## Slide 15: Dynamic Linking
Static linking – system libraries and program code combined by the loader into the binary program image
Dynamic linking –linking postponed until execution time
Small piece of code, stub, used to locate the appropriate memory-resident library routine
Stub replaces itself with the address of the routine, and executes the routine
Operating system checks if routine is in processes’ memory address
  If not in address space, add to address space
Dynamic linking is particularly useful for libraries
System also known as shared libraries
Consider applicability to patching system libraries
  Versioning may be needed

## Slide 16: Contiguous Allocation
Main memory must support both OS and user processes
Limited resource, must allocate efficiently
Contiguous allocation is one early method
Main memory usually into two partitions:
  Resident operating system, usually held in low memory with interrupt vector
  User processes then held in high memory
  Each process contained in single contiguous section of memory

## Slide 17: Contiguous Allocation (Cont.)
Relocation registers used to protect user processes from each other, and from changing operating-system code and data
  Base register contains value of smallest physical address
  Limit register contains range of logical addresses – each logical address must be less than the limit register
  MMU maps logical address dynamically
  Can then allow actions such as kernel code being transient and kernel changing size

## Slide 18: Hardware Support for Relocation and Limit Registers

## Slide 19: Variable Partition
Multiple-partition allocation
  Degree of multiprogramming limited by number of partitions
  Variable-partition sizes for efficiency (sized to a given process’ needs)
  Hole – block of available memory; holes of various size are scattered throughout memory
  When a process arrives, it is allocated memory from a hole large enough to accommodate it
  Process exiting frees its partition, adjacent free partitions combined
  Operating system maintains information about: a) allocated partitions b) free partitions (hole)

## Slide 20: Dynamic Storage-Allocation Problem
First-fit: Allocate the first hole that is big enough
Best-fit: Allocate the smallest hole that is big enough; must search entire list, unless ordered by size
  Produces the smallest leftover hole
Worst-fit: Allocate the largest hole; must also search entire list
  Produces the largest leftover hole
How to satisfy a request of size n from a list of free holes?
First-fit and best-fit better than worst-fit in terms of speed and storage utilization

## Slide 21: Fragmentation
External Fragmentation – total memory space exists to satisfy a request, but it is not contiguous
Internal Fragmentation – allocated memory may be slightly larger than requested memory; this size difference is memory internal to a partition, but not being used
First fit analysis reveals that given N blocks allocated, 0.5 N blocks lost to fragmentation
  1/3 may be unusable -> 50-percent rule

## Slide 22: Fragmentation (Cont.)
Reduce external fragmentation by compaction
  Shuffle memory contents to place all free memory together in one large block
  Compaction is possible only if relocation is dynamic, and is done at execution time
  I/O problem
    Latch job in memory while it is involved in I/O
    Do I/O only into OS buffers
Now consider that backing store has same fragmentation problems

## Slide 23: Paging
Physical address space of a process can be noncontiguous; process is allocated physical memory whenever the latter is available
  Avoids external fragmentation
  Avoids problem of varying sized memory chunks
Divide physical memory into fixed-sized blocks called frames
  Size is power of 2, between 512 bytes and 16 Mbytes
Divide logical memory into blocks of same size called pages
Keep track of all free frames
To run a program of size N pages, need to find N free frames and load program
Set up a page table to translate logical to physical addresses
Backing store likewise split into pages
Still have Internal fragmentation

## Slide 24: Address Translation Scheme
Address generated by CPU is divided into:
  Page number (p) – used as an index into a page table which contains base address of each page in physical memory
  Page offset (d) – combined with base address to define the physical memory address that is sent to the memory unit
  For given logical address space 2m and page size 2n

## Slide 25: Paging Hardware

## Slide 26: Paging Model of Logical and Physical Memory

## Slide 27: Paging Example
Logical address: n = 2 and m = 4. Using a page size of 4 bytes and a physical memory of 32 bytes (8 pages)

## Slide 28: Paging -- Calculating internal fragmentation
Page size = 2,048 bytes
Process size = 72,766 bytes
35 pages + 1,086 bytes
Internal fragmentation of 2,048 - 1,086 = 962 bytes
Worst case fragmentation = 1 frame – 1 byte
On average fragmentation = 1 / 2 frame size
So small frame sizes desirable?
But each page table entry takes memory to track
Page sizes growing over time
  Solaris supports two page sizes – 8 KB and 4 MB

## Slide 29: Free Frames
Before allocation
After allocation

## Slide 30: Implementation of Page Table
Page table is kept in main memory
  Page-table base register (PTBR) points to the page table
  Page-table length register (PTLR) indicates size of the page table
In this scheme every data/instruction access requires two memory accesses
  One for the page table and one for the data / instruction
The two-memory access problem can be solved by the use of a special fast-lookup hardware cache called translation look-aside buffers (TLBs) (also called associative memory).

## Slide 31: Translation Look-Aside Buffer
Some TLBs store address-space identifiers (ASIDs) in each TLB entry – uniquely identifies each process to provide address-space protection for that process
  Otherwise need to flush at every context switch
TLBs typically small (64 to 1,024 entries)
On a TLB miss, value is loaded into the TLB for faster access next time
  Replacement policies must be considered
  Some entries can be wired down for permanent fast access

## Slide 32: Hardware
Associative memory – parallel search
Address translation (p, d)
  If p is in associative register, get frame # out
  Otherwise get frame # from page table in memory

## Slide 33: Paging Hardware With TLB

## Slide 34: Effective Access Time
  Hit ratio – percentage of times that a page number is found in the TLB
An 80% hit ratio means that we find the desired page number in the TLB 80% of the time.
Suppose that 10 nanoseconds to access memory.
  If we find the desired page in TLB then a mapped-memory access take 10 ns
  Otherwise we need two memory access so it is 20 ns
Effective Access Time (EAT)
EAT = 0.80 x 10 + 0.20 x 20 = 12 nanoseconds
implying 20% slowdown in access time
Consider amore realistic hit ratio of 99%,
  EAT = 0.99 x 10 + 0.01 x 20 = 10.1ns
implying only 1% slowdown in access time.

## Slide 35: Memory Protection
Memory protection implemented by associating protection bit with each frame to indicate if read-only or read-write access is allowed
  Can also add more bits to indicate page execute-only, and so on
Valid-invalid bit attached to each entry in the page table:
  “valid” indicates that the associated page is in the process’ logical address space, and is thus a legal page
  “invalid” indicates that the page is not in the process’ logical address space
  Or use page-table length register (PTLR)
Any violations result in a trap to the kernel

## Slide 36: Valid (v) or Invalid (i) Bit In A Page Table

## Slide 37: Shared Pages
Shared code
  One copy of read-only (reentrant) code shared among processes (i.e., text editors, compilers, window systems)
  Similar to multiple threads sharing the same process space
  Also useful for interprocess communication if sharing of read-write pages is allowed
Private code and data
  Each process keeps a separate copy of the code and data
  The pages for the private code and data can appear anywhere in the logical address space

## Slide 38: Shared Pages Example

## Slide 39: Structure of the Page Table
Memory structures for paging can get huge using straight-forward methods
  Consider a 32-bit logical address space as on modern computers
  Page size of 4 KB (212)
  Page table would have 1 million entries (232 / 212)
  If each entry is 4 bytes  each process 4 MB of physical address space for the page table alone
    Don’t want to allocate that contiguously in main memory
  One simple solution is to divide the page table into smaller units
    Hierarchical Paging
    Hashed Page Tables
    Inverted Page Tables

## Slide 40: Hierarchical Page Tables
Break up the logical address space into multiple page tables
A simple technique is a two-level page table
We then page the page table

## Slide 41: Two-Level Paging Example
A logical address (on 32-bit machine with 4K page size) is divided into:
  a page number consisting of 20 bits
  a page offset consisting of 12 bits
Since the page table is paged, the page number is further divided into:
  a 10-bit page number
  a 10-bit page offset
Thus, a logical address is as follows:
where p1 is an index into the outer page table, and p2 is the displacement within the page of the inner page table
Known as forward-mapped page table

## Slide 42: Address-Translation Scheme

## Slide 43: 64-bit Logical Address Space
Even two-level paging scheme not sufficient
If page size is 4 KB (212)
  Then page table has 252 entries
  If two level scheme, inner page tables could be 210 4-byte entries
  Address would look like
  Outer page table has 242 entries or 244 bytes
  One solution is to add a 2nd outer page table
  But in the following example the 2nd outer page table is still 234 bytes in size
    And possibly 4 memory access to get to one physical memory location

## Slide 44: Three-level Paging Scheme

## Slide 45: Hashed Page Tables
Common in address spaces > 32 bits
The virtual page number is hashed into a page table
  This page table contains a chain of elements hashing to the same location
Each element contains (1) the virtual page number (2) the value of the mapped page frame (3) a pointer to the next element
Virtual page numbers are compared in this chain searching for a match
  If a match is found, the corresponding physical frame is extracted
Variation for 64-bit addresses is clustered page tables
  Similar to hashed but each entry refers to several pages (such as 16) rather than 1
  Especially useful for sparse address spaces (where memory references are non-contiguous and scattered)

## Slide 46: Hashed Page Table

## Slide 47: Inverted Page Table
Rather than each process having a page table and keeping track of all possible logical pages, track all physical pages
One entry for each real page of memory
Entry consists of the virtual address of the page stored in that real memory location, with information about the process that owns that page
Decreases memory needed to store each page table, but increases time needed to search the table when a page reference occurs
Use hash table to limit the search to one — or at most a few — page-table entries
  TLB can accelerate access
But how to implement shared memory?
  One mapping of a virtual address to the shared physical address

## Slide 48: Inverted Page Table Architecture

## Slide 49: Oracle SPARC Solaris
Consider modern, 64-bit operating system example with tightly integrated HW
  Goals are efficiency, low overhead
Based on hashing, but more complex
Two hash tables
  One kernel and one for all user processes
  Each maps memory addresses from virtual to physical memory
  Each entry represents a contiguous area of mapped virtual memory,
    More efficient than having a separate hash-table entry for each page
  Each entry has base address and span (indicating the number of pages the entry represents)

## Slide 50: Oracle SPARC Solaris (Cont.)
TLB holds translation table entries (TTEs) for fast hardware lookups
  A cache of TTEs reside in a translation storage buffer (TSB)
    Includes an entry per recently accessed page
Virtual address reference causes TLB search
  If miss, hardware walks the in-memory TSB looking for the TTE corresponding to the address
    If match found, the CPU copies the TSB entry into the TLB and translation completes
    If no match found, kernel interrupted to search the hash table
      The kernel then creates a TTE from the appropriate hash table and stores it in the TSB, Interrupt handler returns control to the MMU, which completes the address translation.

## Slide 51: Swapping
A process can be swapped temporarily out of memory to a backing store, and then brought back into memory for continued execution
  Total physical memory space of processes can exceed physical memory
Backing store – fast disk large enough to accommodate copies of all memory images for all users; must provide direct access to these memory images
Roll out, roll in – swapping variant used for priority-based scheduling algorithms; lower-priority process is swapped out so higher-priority process can be loaded and executed
Major part of swap time is transfer time; total transfer time is directly proportional to the amount of memory swapped
System maintains a ready queue of ready-to-run processes which have memory images on disk

## Slide 52: Swapping (Cont.)
Does the swapped out process need to swap back in to same physical addresses?
Depends on address binding method
  Plus consider pending I/O to / from process memory space
Modified versions of swapping are found on many systems (i.e., UNIX, Linux, and Windows)
  Swapping normally disabled
  Started if more than threshold amount of memory allocated
  Disabled again once memory demand reduced below threshold

## Slide 53: Schematic View of Swapping

## Slide 54: Context Switch Time including Swapping
If next processes to be put on CPU is not in memory, need to swap out a process and swap in target process
Context switch time can then be very high
100MB process swapping to hard disk with transfer rate of 50MB/sec
  Swap out time of 2000 ms
  Plus swap in of same sized process
  Total context switch swapping component time of 4000ms (4 seconds)
Can reduce if reduce size of memory swapped – by knowing how much memory really being used
  System calls to inform OS of memory use via request_memory() and release_memory()

## Slide 55: Context Switch Time and Swapping (Cont.)
Other constraints as well on swapping
  Pending I/O – can’t swap out as I/O would occur to wrong process
  Or always transfer I/O to kernel space, then to I/O device
    Known as double buffering, adds overhead
Standard swapping not used in modern operating systems
  But modified version common
    Swap only when free memory extremely low

## Slide 56: Swapping on Mobile Systems
Not typically supported
  Flash memory based
    Small amount of space
    Limited number of write cycles
    Poor throughput between flash memory and CPU on mobile platform
Instead use other methods to free memory if low
  iOS asks apps to voluntarily relinquish allocated memory
    Read-only data thrown out and reloaded from flash if needed
    Failure to free can result in termination
  Android terminates apps if low free memory, but first writes application state to flash for fast restart
  Both OSes support paging as discussed below

## Slide 57: Swapping with Paging

## Slide 58: Example: The Intel 32 and 64-bit Architectures
Dominant industry chips
Pentium CPUs are 32-bit and called IA-32 architecture
Current Intel CPUs are 64-bit and called IA-64 architecture
Many variations in the chips, cover the main ideas here

## Slide 59: Example: The Intel IA-32 Architecture
Supports both segmentation and segmentation with paging
  Each segment can be 4 GB
  Up to 16 K segments per process
  Divided into two partitions
    First partition of up to 8 K segments are private to process (kept in local descriptor table (LDT))
    Second partition of up to 8K segments shared among all processes (kept in global descriptor table (GDT))

## Slide 60: Example: The Intel IA-32 Architecture (Cont.)
CPU generates logical address
  Selector given to segmentation unit
    Which produces linear addresses
  Linear address given to paging unit
    Which generates physical address in main memory
    Paging units form equivalent of MMU
    Pages sizes can be 4 KB or 4 MB

## Slide 61: Logical to Physical Address Translation in IA-32

## Slide 62: Intel IA-32 Segmentation

## Slide 63: Intel IA-32 Paging Architecture

## Slide 64: Intel IA-32 Page Address Extensions
32-bit address limits led Intel to create page address extension (PAE), allowing 32-bit apps access to more than 4GB of memory space
  Paging went to a 3-level scheme
  Top two bits refer to a page directory pointer table
  Page-directory and page-table entries moved to 64-bits in size
  Net effect is increasing address space to 36 bits – 64GB of physical memory

## Slide 65: Intel x86-64
Current generation Intel x86 architecture
64 bits is ginormous (> 16 exabytes)
In practice only implement 48 bit addressing
  Page sizes of 4 KB, 2 MB, 1 GB
  Four levels of paging hierarchy
Can also use PAE so virtual addresses are 48 bits and physical addresses are 52 bits

## Slide 66: Example: ARM Architecture
Dominant mobile platform chip (Apple iOS and Google Android devices for example)
Modern, energy efficient, 32-bit CPU
4 KB and 16 KB pages
1 MB and 16 MB pages (termed sections)
One-level paging for sections, two-level for smaller pages
Two levels of TLBs
  Outer level has two micro TLBs (one data, one instruction)
  Inner is single main TLB
  First inner is checked, on miss outers are checked, and on miss page table walk performed by CPU

## Slide 67: End of Chapter 9